## Slide 1: Technical insight into the Waste-to-Energy initiative in Lao PDR
Brahmanand Mohanty, Ph.D.
Workshop on
Waste-to-energy, Industrial waste reuse and prevention solutions
Asia-Pacific Climate Week
Singapore, 12 July 2018

## Slide 2: Industrial waste-to-energy initiative in Lao PDR
Project Objective: To reduce GHG emission in Lao PDR’s industries by promoting the production and usage of high-quality solid biofuel for thermal energy applications
Agricultural and agro-industrial waste
Rural industries and households
Agri-residue resources in Laos can theoretically meet 238% of the primary energy use.
ADB sponsored study (2013)
Introduction of technologies, economic models and policies for:
  Conversion of traditional agricultural and agro-industrial waste into modern biomass energy
  Efficient utilization of modern biomass energy to avoid the import of fossil fuels, improve human health, reduce deforestation and lower greenhouse gas emissions

## Slide 3: Industrial waste-to-energy initiative in Lao PDR
Situation analysis:
  Traditional fuels (wood and agricultural waste):
    Major source of energy, often not correctly priced, not easy to transport and use
  Crude technologies for combustion:
    Inefficient fuel use, low-quality product, poor air quality, affecting human health & the environment
  Over-exploitation of natural resources:
    Deforestation
  Some industries shifting to fossil fuels:
    Improve product quality and the environment but increase import dependence
Barriers / challenges:
  Lack of awareness and exposure to suitable technologies and practices
  Limited expertise to adopt clean technology solutions
  Lack of supportive policy framework for efficient use of local energy resources
  Lack of tools and mechanisms to develop bankable proposals

## Slide 4: Industrial waste-to-energy initiative in Lao PDR
UNIDO-GEF’s response to overcome the challenges:
  Propose solutions to
    Convert wood and agro-industrial waste into modern energy sources (pellets) that can be easily stored, transported and used efficiently in suitably designed burners, stoves and boilers
  Such solutions allow small and medium industries to
    Reduce dependence on fossil fuels
    Avoid over-exploiting traditional energy sources and reduce human drudgery
    Carry out efficient production and improve product quality
    Improve the air quality in the work place and contribute to better human health
    Mobilize expertise to strengthen capacities of different stakeholders (producers, users, technology providers, banks and policy makers)

## Slide 5: Industrial waste-to-energy initiative in Lao PDR
The above technologies are quite common in neighboring Thailand and Vietnam but not yet in Laos:
  Small country with low population dispersed over a fairly large territory
  Easy access to traditional fuel at very low cost and averse to high first-cost
  Low level of industrial development and lack of support for research and innovation
  SMIs have poor knowledge of market to sell better quality product at higher price
UNIDO-GEF’s role:
  Initiate technology demonstration through technology transfer from neighboring countries, with involvement of local stakeholders, including R&D entities
  Hold sensitization seminars to showcase the technology and highlight the economic, social (job creation, gender mainstreaming) and environmental co-benefits
  Support the government in creating a Biomass Technology Information and Learning Centre (BTILC) for strengthening institutional and human capacity
  Provide feedback to policy makers on suitable regulatory and incentive measures

## Slide 6: From agro-waste to useful energy: value chain
Agriculture and Wood Sources
Pellet production plant
Customers
Agro/Wood factories
Emphasis on:
Technology support, capacity building and inclusive development
South-South cooperation
  Ensure suitability of technology to the context of the country

## Slide 7: Mapping of resources (waste from agro-industries)
Bokeo
Laung
namtha
Oudomxay
Xayaboury
Phongsaly
Luangphabang
Huaphan
Xiengkhuang
Xaysomboun
Vientiane
Vientiane Capital
Bolikhamxay
Khammuane
Savannakhet
Saravan
Sekong
Champasak
Attapeu
>80,000 ton per year
60,001-80,000 ton per year
20,001-60,000 ton per year
< 20,000 ton per year
Corn cob
Bagasse
Bokeo
Laung
namtha
Oudomxay
Xayaboury
Phongsaly
Luangphabang
Huaphan
Xiengkhuang
Xaysomboun
Vientiane
Vientiane Capital
Bolikhamxay
Khammuane
Savannakhet
Saravan
Sekong
Champasak
Attapeu
>150,000 ton per year
100,001-150,000 ton per year
50,001-100,000 ton per year
< 50,000 ton per year
Bokeo
Laung
namtha
Oudomxay
Xayaboury
Phongsaly
Luang
phabang
Huaphan
Xiengkhuang
Xaysom
boun
Vientiane
Vientiane Capital
Bolikhamxay
Khammuane
Savannakhet
Saravan
Sekong
Champasak
Attapeu
>150,000 ton per year
100,001-150,000 ton per year
50,001-100,000 ton per year
< 50,000 ton per year
Rice Husk

## Slide 8: Selection of ideal site and sizing of pellet plant
Vientiane
Salt factory
Source of agro-industrial waste
Factories using traditional fuel inefficiently
>500 Ton per month
100-400 Ton per month
< 100 Ton per month
Objective: Minimize transportation while closing the loop (circular economy)

## Slide 9: Bio-Pellet production technologies

## Slide 10: Bio-Pellet consumption technologies (1)
Fuel hopper
Burner
Burner control
Boiler control
Screw feeder
Air compressor
Flue gas stack

## Slide 11: Bio-Pellet consumption technologies (2)
This is in synergy with the World Bank initiative addressing a number of Sustainable Development Goals, including good health and well-being, gender equality, climate action

## Slide 12: Co-benefits from a typical 2 t/h pellet plant
Create 20 new jobs
Avoid 10,000 tons of coal/year
Provide clean cooking for 18,000 families
Reduce 14,500 tons/year of GHG emissions
Protect
470 ha of forest land
Improve health of 25,000 women & children

## Slide 13: Lessons learned to replicate best practices
Low-density agro-industrial residue has a huge potential to be used as modern energy source in less developed countries
Government policy should favor closing the loop at the local level
Technological solutions should be dictated by inclusive industrial development goals (economic, social, energy security, environment)
South-South cooperation can generally make technology transfer more easily acceptable (e.g. replication in other LDCs like Cambodia)
Awareness raising and capacity enhancement should be a constant preoccupation of national decision-makers

## Slide 14: Thank you for your attention